## Slide 1
Analysis of Image Sensing System Challenges
Acquisition Phenomena, Mathematical Noise Models & Analytical Restoration Frameworks
A Comprehensive Technical Analysis of Optical Acquisition Bottlenecks, Noise Physics, and Hardware-Software Mitigation Strategies

## Slide 2
IMAGE SENSING SYSTEMS
1. The Image Acquisition Pipeline & Degradation Architecture
1. Photonic Scene
Radiance I(x,y) Photon arrive statistics
2. Optical Lens
Aberrations, Vignetting Point Spread Function h(x,y)
3. Photodetector
Photon-to-electron (QE) Shot Noise & Thermal Dark Current
4. Readout & ADC
Amplifier Read Noise Quantization & Clipping
Unified Acquisition Mathematical Model
g(x,y) = h(x,y) * f(x,y) + η(x,y)
Where g(x,y) is the observed degraded digital image, h(x,y) is the system Point Spread Function (PSF) representing optical and sensor spatial blur, f(x,y) is the true scene radiance, and η(x,y) is the additive superposition of read noise, shot noise, and dark current.

## Slide 3
IMAGE SENSING SYSTEMS
2. Fundamental Physical Noise Sources in Photodetectors
Photon Shot Noise (Quantum Limit)
• Physics: Discrete arrival of photons governed by Poisson statistics. • Formula: P(k) = (λt)^k * e^(-λt) / k! • Characteristic: Variance equals the mean signal (σ² = μ). Signal-to-Noise Ratio scales as √μ. • Impact: Dominates at high light levels; fundamental physical limit that cannot be eliminated.
Dark Current & Thermal Generation
• Physics: Thermally generated electron-hole pairs without photon illumination. • Shockley-Read-Hall Model: Idark ∝ T^(1.5) * exp(-Eg / 2kB*T) • Impact: Exponentially increases with sensor temperature T; causes fixed pattern noise and dark shot noise floor in long exposures.
Read Noise & ADC Quantization
• Physics: Thermal and flicker noise in output transistor amplifiers plus A/D conversion error. • Superposition: Ntotal = √(σshot² + σdark² + σread² + σADC²) • Impact: Establishes absolute low-light sensitivity limit.

## Slide 4
IMAGE SENSING SYSTEMS
3. Spatial & Temporal Acquisition Distortions
Distortion Type | Mathematical / Analytical Model | Physical Impact & Artifacts
Optical Blur (PSF) | MTF(f) = ¦F{h(x,y)}¦ | Attenuates high spatial frequencies; limits overall sensor contrast and sharpness.
Vignetting | I(θ) = I₀ · cos⁴(θ) | Radial light intensity attenuation towards image periphery due to lens geometry.
Motion Blur | g(x,y) = ∫₀ᵀ f(x - vx·t, y - vy·t) dt | Spatial integration over finite exposure time T creates linear motion smearing.
Rolling Shutter Skew | Δy(t) = vy · trow · y | Sequential row readout causes geometric warping/skew in high-speed moving targets.

## Slide 5
IMAGE SENSING SYSTEMS
4. Analytical Diagnostic Tools for Sensor Assessment
Photon Transfer Curve (PTC)
Plots signal variance (σ²) vs. mean output signal (μ). • Extracts conversion gain (e⁻/DN) • Measures read noise floor • Determines Full Well Saturation (FWC)
Slanted-Edge MTF Analysis
Differentiates Edge Spatial Response (ESR) → Line Spread Function (LSF) → Fourier Transform. • Quantifies system Modulation Transfer Function (MTF) spatial resolution limit.
Flat-Field & Dark Profiling
Captures uniform light frames (Iflat) and zero-flux dark frames (Idark). • Quantifies Fixed-Pattern Noise (FPN) • Measures Dark Current Non-Uniformity (DCNU)

## Slide 6
IMAGE SENSING SYSTEMS
5. System Mitigation & Restoration Frameworks
Hardware-Level Mitigations
• Thermo-Electric Cooling (TEC / Peltier): Lowers operational temperature T to exponentially reduce dark current generation. • Global Shutter Architecture: Integrates storage capacitors at each pixel node to capture entire frame simultaneously, eliminating rolling shutter spatial skew. • Back-Side Illumination (BSI): Moves wiring layers behind photodiode layer, boosting Fill Factor & Quantum Efficiency (>90%).
Software & Algorithmic Restoration
• Flat-Field Correction (FFC): Corrects spatial non-uniformities & vignetting: Icorrected = [(Iraw - Idark) / (Iflat - Idark)] × μflat • Wiener Deconvolution Filter: Optimal MSE restoration under noise: F_hat(u,v) = [ H*(u,v) / (|H(u,v)|² + Sη/Sf) ] · G(u,v) • Correlated Double Sampling (CDS): Subtracts pixel reset voltage from data voltage to cancel kTC reset noise.

## Slide 7
IMAGE SENSING SYSTEMS
6. Key Takeaways & Engineering Trade-Offs
1. Acquisition Bottlenecks are Multiphysics
Degradation stems from quantum mechanics (shot noise), thermodynamics (dark current), wave optics (diffraction/MTF), and readout electronics.
2. Spatial vs. Dynamic Range Trade-off
Shrinking pixel size improves spatial resolution but reduces Full Well Capacity (FWC), degrading dynamic range and SNR.
3. Noise Floor Superposition
System performance in low-light is strictly governed by read noise and dark current floor, while bright-light performance is governed by photon shot noise.
4. Co-Design is Essential
Hardware mechanisms (TEC cooling, BSI sensors, Global Shutter) must be paired with algorithmic pipelines (FFC, Wiener deconvolution, CDS) for optimal imaging fidelity.