## Slide 1
Intensity Resolution in Digital Image Processing
Problem-Based Scenarios, Quantization Dynamics, & Technical Analysis
Comprehensive evaluation of radiometric bit depth, false contouring, and diagnostic precision thresholds.

## Slide 2
1. Fundamentals of Intensity Resolution
Radiometric Sampling & Quantization Mathematics
Core Concept
• Intensity (Radiometric) Resolution defines the smallest discernible change in shade or gray level in a digital image.
• It depends directly on the bit depth (k) assigned to quantize continuous sensor amplitude values.
• Higher bit depth increases dynamic range accuracy, eliminating signal clipping and subtle detail loss.
Mathematical Formulations
Discrete Gray Levels (L):
L = 2^k
Quantization Step Size (Δ):
Δ = (I_max - I_min) / 2^k
Signal-to-Quantization-Noise (SQNR):
SQNR ≈ 6.02k + 1.76 dB
Key Rule of Thumb:
Each added bit adds +6.02 dB SQNR and doubles gray resolution.

## Slide 3
2. Problem Scenario 1: Medical CT Diagnostics
Brain Ischemic Stroke Differentiation (-1000 HU to +2000 HU Range)
Clinical Challenge:
A radiologist must detect an early ischemic lesion (+28 HU) surrounded by healthy brain tissue (+35 HU). Delta intensity = 7 HU across a total dynamic CT range of 3000 HU.
8-Bit System (256 Levels)
• Step Size (Δ): 3000 / 256 = 11.72 HU
• Quantization Error: ±5.86 HU
• Analysis: The 7 HU tissue difference is SMALLER than a single step size (11.72 HU).
• Clinical Result: DIAGNOSTIC FAILURE. Ischemic stroke is quantized into the exact same bin as healthy tissue.
12-Bit System (4096 Levels)
• Step Size (Δ): 3000 / 4096 = 0.73 HU
• Quantization Error: ±0.37 HU
• Analysis: The 7 HU difference spans ~10 discrete gray levels.
• Clinical Result: DIAGNOSTIC SUCCESS. High clarity; stroke boundaries and low-contrast details are fully resolved.

## Slide 4
3. Problem Scenario 2: False Contouring Artifacts
Quantization Thresholds & Human Visual System (HVS) Perception
Mechanism of False Contouring (Posterization)
Smooth Gradient Compression: When a continuous smooth intensity gradient (e.g., sky or tissue scan) is requantized from 8-bit (256 levels) down to 3-bit (8 levels), step size jumps from Δ = 1 to Δ = 32 units.
Perceptual Discontinuity: Instead of a continuous ramp, wide adjacent pixel regions are mapped to identical gray values, creating steep jump lines (ridge lines).
Weber's Law Violation: The Human Visual System (HVS) detects intensity step jumps exceeding ~1% to 2% of background brightness. At 3-bit depth, step jumps equal 12.5%, drastically triggering false contour boundaries.
Dithering Remedy: Adding controlled pseudorandom noise prior to low-bit quantization breaks up distinct banding at the cost of slight grain.

## Slide 5
4. Bit Depth Performance Matrix
Comprehensive Breakdown Across Radiometric Levels
Bit Depth (k) | Gray Levels (2^k) | SQNR (dB) | Perceptual Quality | Typical Applications
1-bit | 2 | 7.78 dB | Binary / High Contrast | Barcodes, document scanners, text
4-bit | 16 | 25.84 dB | Severe False Contouring | Legacy embedded displays
8-bit | 256 | 49.92 dB | Standard Quality (HVS Limit) | Consumer Web, RGB images, MP4 video
12-bit | 4096 | 74.00 dB | High Precision / Scientific | Medical CT, MRI, Digital X-Ray
16-bit | 65536 | 98.08 dB | Ultra-High Dynamic Range | Satellite Remote Sensing, Astronomical RAW